## Slide 1
DSP391m · REPORT 1 · PROJECT PROPOSAL
Forecasting Flood Risk
1–3 Days Ahead
Huong River, Hue — from open hydro-meteorological data
Team
Dang Nguyen Giap · Hoang Anh Duc · Le Thi Huyen
Gauging station
Kim Long · GloFAS cell 16.45 N, 107.50 E
Week 2 · 17 September 2026
Notes: Good morning. Our project forecasts flood risk one to three days ahead for the Huong River in Hue, using only open data. Central Vietnam is the most flood-affected region in the country, but local gauging coverage is thin. We ask whether freely available global data can close part of that gap. I will cover the subject and its big-data context, the problem and the analytics approach we chose, and how we collect the data.

## Slide 2
SUBJECT & CONTEXT
Why the Huong River basin
Central Vietnam is the country's most flood-affected region; Hue sits on a short, steep basin where floods rise within a day.
Riverside communes suffer repeated damage, yet local gauging and commune-level warning remain sparse.
Official alerts are issued as water-level stages BĐ I / II / III — the language local authorities already act on.
Open global datasets now cover this basin at daily resolution, free and without an API key.
Research questions
Can river discharge be predicted 1, 2 and 3 days ahead from gridded rainfall and past discharge — and at what error?
How well can a classifier flag days that exceed an official flood-alert stage?
Which sub-basins carry the highest seasonal risk?
Official alert stages
Kim Long station · water level above datum
BĐ I
1.00 m
BĐ II
2.00 m
BĐ III
3.50 m
Decision 05/2020/QD-TTg. Cross-checked against five bulletins of the Hue Hydro-Meteorological Station.
DSP391m · Report 1 — Project Proposal | 2
Notes: The Huong basin is about 2,830 square kilometres — small and steep, so floods rise and fall inside a day or two. That short response time is exactly what makes a one-to-three-day forecast useful, and also what makes it hard. On the right are the official alert stages at Kim Long: one, two and three and a half metres. We anchor our target variable to these stages rather than inventing our own scale, because these are the numbers local authorities already act on.

## Slide 3
CONTEXT OF BIG DATA
What makes this a data problem
Volume alone does not define big data. This project meets four of the classic dimensions — each with a concrete figure from the data we have already collected.
Volume
42 years of daily discharge and 11 years of hourly rainfall across 68 grid points — about 1,500 Parquet files.
Variety
Simulated discharge, reanalysis rainfall, archived rainfall forecasts, river geometry, legal thresholds and news bulletins.
Velocity
Forecasts are re-issued every few hours; an automated job pulls a new 7-day forecast every morning.
Veracity
Discharge is model output, not measurement. Reservoir releases are unmodelled. Both must be stated, not hidden.
Value. The output is not a number but a decision: which alert stage a commune should expect tomorrow, and how much confidence to place in it.
DSP391m · Report 1 — Project Proposal | 3
Notes: We deliberately avoid claiming this is big data just because it is large. Volume is moderate — about fifteen hundred files. What actually makes it a data-engineering problem is variety and veracity. Six different source types have to be reconciled onto one daily timeline, and the discharge series is simulated rather than measured. We treat that as a stated limitation, not a footnote.

## Slide 4
PROBLEM STATEMENT
Two linked problems, one pipeline
1
Regression — how much water?
Predict daily mean discharge in m³/s at horizons of 1, 2 and 3 days. Continuous target; evaluated with RMSE, MAE, NSE and KGE.
2
Classification — which alert stage?
Predict whether each day exceeds BĐ I, II or III. Positive days are rare — roughly 1–3 % — so accuracy is banned; we use POD, FAR, CSI and PR-AUC.
3
The bridge between them
Official stages are water levels in metres; the data is discharge in m³/s. A calibration mapping from documented flood peaks converts one to the other.
Constraint that shapes everything: no measured water-level series is available to us, so the level-to-discharge mapping must be built indirectly from published flood peaks.
DSP391m · Report 1 — Project Proposal | 4
Notes: There are two targets. The regression problem asks how much water; the classification problem asks which alert stage. They are linked by a unit conversion that is not trivial: the legal thresholds are water levels in metres, our data is discharge in cubic metres per second, and we could not obtain a measured rating curve. So we build that mapping from documented flood peaks instead — and we name it a calibration mapping, not a rating curve, because it absorbs model error as well as channel geometry.

## Slide 5
ANALYTICS APPROACH
Primarily predictive
SUPPORTING
Descriptive
What happened?
Supporting. Seasonality, rainfall–discharge lag, historical flood events.
PARTIAL
Diagnostic
Why did it happen?
Partial. SHAP attributes each warning to rainfall, antecedent wetness or season.
CORE
Predictive
What will happen?
Core. Discharge and alert stage 1–3 days ahead. Both research questions live here.
OUT OF SCOPE
Prescriptive
What should we do?
Out of scope. Evacuation decisions need authority and liability we do not have.
A global forecast system already publishes discharge for this cell. Our contribution is to correct it locally and translate it into Vietnam's own alert stages at sub-basin scale — not to replace it.
DSP391m · Report 1 — Project Proposal | 5
Notes: Of the four analytics types, our work is primarily predictive. Descriptive analysis supports it and diagnostic comes through model explanation. We deliberately exclude prescriptive: recommending an evacuation is a decision that needs legal authority we do not have, and claiming otherwise would be irresponsible for a student project. The last line is important — a global system already forecasts this cell, so our contribution is local correction and translation into Vietnamese alert stages, not replacement.

## Slide 6
DATA REQUIREMENTS
Six inputs, one daily table
Dataset | Role in the model | Span / resolution | Status
River discharge (GloFAS v4) | Target variable and lag features | 1984–2026 · daily · ~5 km | Collected
Rainfall, temperature, wind (ERA5) | Main predictors, aggregated by sub-basin | 2010–2026 · daily & hourly | Collected
Archived rainfall forecasts | Operational scenario — what was knowable in advance | 2022–2026 · daily | Collected
River centre-lines (OpenStreetMap) | Assign grid cells to the correct river | Current snapshot | Collected
Legal alert thresholds | Defines the classification target | Decision 05/2020/QD-TTg | Verified
Documented flood peaks | Calibrates water level to discharge | ≥ 15 events, 1999–2026 | In progress
All sources are open and free. Open-Meteo data is published under CC BY 4.0 and is cited accordingly; the total project cost is zero.
The last row is the critical path: without documented flood peaks the alert-stage target cannot be defined, so the classification problem cannot be evaluated.
DSP391m · Report 1 — Project Proposal | 6
Notes: Six inputs feed one daily analysis table. Five of them are already on disk. The one still in progress is the set of documented flood peaks, and it is the critical path: without it we cannot convert the legal water-level thresholds into discharge, which means the classification target does not exist. That is a manual reading task — bulletins and disaster reports — and it cannot be automated away.

## Slide 7
COLLECTION METHOD
How the data is collected
1
Select
Scan a 361-cell grid; pick the cell whose inferred catchment matches the real basin
→
2
Crawl
Independent tasks, one Parquet file each; retry, cache and checkpoint
→
3
Clean
Normalise to Vietnam time, aggregate hourly to daily, validate and fail loudly
→
4
Assemble
Average rainfall over three sub-basins, build lag features, prevent leakage
Design decisions that made it work
Every task writes its own file, so an interrupted run resumes for free and never re-requests what it already has.
Request pacing adapts to the server: it widens on rate-limit responses and tightens again when the run is clean.
A lock file prevents two crawlers running at once — our own duplicate processes, not the provider, caused every rate-limit error we saw.
Manual collection is planned as manual: reading bulletins for flood peaks is scheduled work, not an afterthought.
DSP391m · Report 1 — Project Proposal | 7
Notes: Collection is a four-stage pipeline. The engineering detail worth a minute is the third bullet. We spent time diagnosing rate-limit errors and blaming the data provider, when in fact our own shell had left three crawler processes running in parallel, competing with each other. With a single process the entire collection finished in about thirty-five minutes with no errors at all. The lesson we wrote into our documentation: when you see rate limiting, count your own processes first.

## Slide 8
FEASIBILITY — ALREADY DEMONSTRATED
The proposal is not hypothetical
6,087 × 71
rows × columns in the assembled daily table
2,929 mm
mean annual rainfall — matches Hue's climate
0.790
peak rainfall–discharge correlation, at 1-day lag
7 %
catchment area error for the selected grid cell
Chart: Rainfall leads discharge by one day
| 0 d | 1 d | 2 d | 3 d | 4 d | 5 d | 6 d | 7 d
Correlation with discharge | 0.641 | 0.79 | 0.608 | 0.382 | 0.284 | 0.233 | 0.184 | 0.149
What this establishes
The data is obtainable, and the physical signal we intend to model is present and strong.
Single-day rainfall outperforms 3-, 5- and 7-day accumulations — the basin responds fast, which supports a short forecast horizon.
Baselines are already measured, so the model has a real bar to clear rather than an assumed one.
A scheduled job has issued a fresh forecast every morning for three consecutive days.
DSP391m · Report 1 — Project Proposal | 8
Notes: We want to show this proposal is not speculative. The data is collected, the table is assembled, and the signal is there: rainfall leads discharge by exactly one day with a correlation of point seven nine. Notice that single-day rainfall beats every multi-day accumulation — the basin responds fast, which is physically consistent with its small steep geometry and supports our short forecast horizon. We have also measured our baselines, so when we report model performance later there will be a real reference point.

## Slide 9
DELIVERABLES & SCHEDULE
What we submit, and when
IEEE-format report
PDF, two-column IEEE template. Introduction, problem statement, objectives, literature review, methodology, timeline and risks.
Oral presentation
Delivered in English with this slide deck. Every team member must be able to explain the whole project, not only their own part.
Both deliverables are due in week 2. Report 1 carries 10 % of the course grade.
Milestones across the nine-week term
Report 1
Proposal
26 Sep
10 %
Report 2
Data & exploratory analysis
09 Oct
20 %
Report 3
Modelling & evaluation
02 Nov
40 %
Report 4
Final consolidated report
10 Nov
10 %
Viva
Individually assessed
13–16 Nov
20 %
DSP391m · Report 1 — Project Proposal | 9
Notes: Two deliverables for this slot: the IEEE-format report as a PDF, and this presentation in English. On the right is the full nine-week schedule. Report 3 carries forty percent and the viva is assessed individually, which is why our team agreed that every member has to be able to explain the whole project, not just the part they built.

## Slide 10
IN ONE SENTENCE
We correct and localise an open global flood forecast into Vietnam's own alert stages for the Huong River, one to three days ahead.
Next three steps
Complete the flood-event record that unlocks the alert-stage target.
Train the forecasting model and beat the measured baselines.
Test whether reservoir operation explains the anomalies we found.
Stated plainly in the report
Discharge data is simulated, not measured.
The 5 km grid cannot resolve the neighbouring Bo River, so the study covers one station.
This is academic work, not an official warning service.
Thank you — questions welcome
Notes: To close: our contribution in one sentence is correction and localisation, not replacement. Three next steps, and three limitations we state openly rather than let a reviewer find. The most important is the second one — the five kilometre grid cannot separate the neighbouring Bo River, so we narrowed the study to one station rather than pretend to cover two. Thank you; we are happy to take questions.